## Slide 1: Fundamentals of Computer networks labs and practices
Dr.Haitham A. El-Ghareeb Computer Networks Fundamentals

## Slide 2: Internet Lab
Basics of Computer Networks

## Slide 3: Configuring TCP/IP Protocol
View the installed networking components and protocols:

## Slide 4: Assign IP address manually
Set IP address
Set Subnet mask
Set IP default-Gateway
Set DNS server
Notes: 1) Go to Start and click on Control Panel. 2) Control Panel window will appear. Double click on Network Connections. 3) Network Connections window will appear. Right click correct Local Area Connection by identifying correct network card and click Properties. 4) Select Internet Protocol (TCP/IP). Click on Properties.

## Slide 5: Assign IP address Automatic
The Device get the IP address through the DHCP Server.

## Slide 6: ipconfig
ipconfig is a command line utility in Microsoft Windows.
ipconfig allows you to get the IP address information of a Windows computer
  MAC Address
  IP address
  Default gateway
  Subnet mask
  DNS server
Notes: C:\Users\nour>ipconfig
Windows IP Configuration
Ethernet adapter Local Area Connection:
Connection-specific DNS Suffix . :
Link-local IPv6 Address . . . . . : fe80::df8:969c:fdbf:cb4%9
IPv4 Address. . . . . . . . . . . : 163.121.12.207
Subnet Mask . . . . . . . . . . . : 255.255.255.0
Default Gateway . . . . . . . . . : 163.121.12.1
--------------------------------------------------------------------------------------------------
C:\Users\rania>ipconfig /all
Windows IP Configuration
Host Name . . . . . . . . . . . . : rania
Primary Dns Suffix . . . . . . . :
Node Type . . . . . . . . . . . . : Hybrid
IP Routing Enabled. . . . . . . . : No
WINS Proxy Enabled. . . . . . . . : No
Ethernet adapter Local Area Connection:
Connection-specific DNS Suffix . :
Description . . . . . . . . . . . : Broadcom NetXtreme 57xx Gigabit Controlle
r
Physical Address. . . . . . . . . : 00-13-72-A5-12-FE
DHCP Enabled. . . . . . . . . . . : No
Autoconfiguration Enabled . . . . : Yes
Link-local IPv6 Address . . . . . : fe80::df8:969c:fdbf:cb4%9(Preferred)
IPv4 Address. . . . . . . . . . . : 163.121.12.207(Preferred)
Subnet Mask . . . . . . . . . . . : 255.255.255.0
Default Gateway . . . . . . . . . : 163.121.12.1
DNS Servers . . . . . . . . . . . : 4.2.2.2
213.131.65.20
NetBIOS over Tcpip. . . . . . . . : Enabled

## Slide 7: TCP/IP Configuration
>ipconfig //give detail on your network settings

## Slide 8: TCP/IP Configuration
>ipconfig /all

## Slide 9: TCP/IP Configuration
ipconfig /all
  This is the main network tool. Using without parameters gives you basic information about your network. With the all parameters, a more detailed information about DNS, DHCP, and other network settings appears.
ipconfig /renew
  This command renews the IP that a DHCP server has assigned to your computer. This is the command that Windows uses when it tells you that is trying to solve a problem with the network.
ipconfig /flushdns
  Your computer has a table with the names of computers and their corresponding IP addresses. This command will remove all the entries on that table. It’s very useful if you change your DNS servers.
ipconfig /displaydns
  This command display the content of the table we were talking before.

## Slide 10: APIPA
Automatic Private IP Addressing
APIPA feature, when installed – will automatically assign an IP to a computer if it is:
  Configured to obtain IP address automatically from DHCP
  And there is no DHCP server present or the DHCP server is not available
IANA (Internet Assigned Numbers Authority) has reserved private IP addresses in the range of 169.254.0.0 – 169.254.355.355

## Slide 11: Internet Services
The World Wide Web: HTTP
File Transfer: FTP
Electronic Mail service: IMAP, POP3, SMTP
Naming Service: DNS
Telnet Service

## Slide 12: Web Servers and Clients
Web Servers
IIS: Internet Information Services
Apache Web server
Web Clients
Browsers

## Slide 13: Browser as a web client
Use Internet Browser as WEB client.

## Slide 14: Dealing with FTP protocol
We need to have :
FTP Server
  User account
  Home Directory
  Permission
FTP Client

## Slide 15: Bullet Proof FTP Server

## Slide 16: Add User Account
Add user account: Setupaccount

## Slide 17: FTP Client
CMD
Internet Explorer
Third Party Program (Cute FTP)

## Slide 18: FTP Client CMD
ftp >open ip //enter username and password
get filename // download file& save in the current directory
mget filename1 filename2 //download multi files
put file name
hash // to see progress bar during process of download
disconnect //close session
bye // close ftp service

## Slide 19: MS Windows built-in FTP client
open
ls
cd
bin
get
mget
Put
bye
Try these commands

## Slide 20: Browser as a FTP client

## Slide 21: Cute FTP Client

## Slide 22: host address : IP of FTP server

## Slide 23: user name and password of client which created on server

## Slide 24: Drag & drop from server to Desktop

## Slide 25: Naming Services
DNS

## Slide 26: URL
URL is Universal Resource Locator
Protocol : HTTP or FTP

## Slide 27: DNS
At the beginning they use Hosts file
It maps the IP addresses to host names
It is found at “C:\Windows\System32\drivers\etc”
Then they make DNS Server to centralize the Domain Name Servers.
Servers are used to convert the addresses we see and read into IP addresses and vice-versa.

## Slide 28: nslookup
With this tool you can check your DNS servers. For example, imagine you are experiencing a problem with your current DNS and it cannot resolve the address www.helghareeb.me
You can test it with nslookup and use other DNS servers to try to resolve the address.
This program can inform about a PC name given his IP address.

## Slide 29: nslookup

## Slide 30: Remote Administration
Remote Desktop

## Slide 31: Windows Built-in Remote Desktop

## Slide 32: TCP/IP Labs
Advanced Commands

## Slide 33: ARP
This tool handles the resolution of a IP to a physical address.
The command gives a list of IPs and physical addresses on your local network.
Run the following command to view the contents of the arp cache
  c:\>arp -a
To add a static entry write the command
  c:\>arp -s 157.55.85.212 00-aa-00-62-c6-09
To delete the arp cache write the command
  c:\>arp -d

## Slide 34: Routing Table Commands
To view the local routing table, write the command
  C:/>route print
To add a route to the routing table, write the command
  C:\>route add 157.0.0.0 mask 255.0.0.0 157.55.80.1
To add a default route, write the command
  C:\>route add 0.0.0.0 mask 0.0.0.0 163.121.25.1
The "metric" switch can be added to the end of the last commands to differentiate between the routes to the same destinations
To delete a certain route, write the command
  C:\>route delete 157.0.0.0

## Slide 35: Ping Command
To check the connectivity with a remote host
  C:\>ping 163.121.25.40
To continue ping operation, just add the switch "-t”
  C:\>ping 163.121.25.40 –t
  c:\>ping -t 163.121.25.40
To control the size of pinging packets, just add the switch "-l” followed by the required packet size
  C:\>ping 163.121.25.40 -l 2000
To control the number of pinging packets, just add the switch "-n" followed by the required packet number
  C:\>ping 163.121.25.40 -n 7

## Slide 36: Ping, Tracert, PathPing
ping
  The easiest way to know if one of your computers is connected to the network.
tracert
  Informs about the route to a remote host. The problem about tracert is that this uses a specific port that can be blocked in the route.
  If you want to know if you can establish a connection between you and a router port use:
pathping
  A better version of tracert that gives you statics about packet lost and latency.

## Slide 37: Opened Ports and Sessions
netstat -nab
  With this basic command, you can know every open port on your computer and the executable that has the port opened. In Windows 7 this command needs Administration rights (Click Start, type cmd, right click cmd.exe and click Run as administrator.)
netstat -r
  Display the routing table

## Slide 38: Port Scanning
LAN Port Scanner

## Slide 39: Windows Networking
Advanced Commands

## Slide 40: Advanced Commands
To quickly reset your NIC back to DHCP with no manual settings, run this command:
  netsh int ip reset all
To quickly generate a text summary of your system, run this command:
  systeminfo | more
To see all network connections your client has open, run this command:
  net use
To see your routing table, run either of these commands:
  route print
  netstat –r

## Slide 41: Advanced Commands
Need to run a trace, but don’t have Netmon or Wireshark, and aren’t allowed to install either one? Run this command:
  netsh trace start capture=yes tracefile=c:\capture.etl
  netsh trace stop
To quickly open a port on the firewall, run this command, changing the name, protocol, and port to suit. This example opens syslog:
  netsh firewall set portopening udp 161 syslog enable all
To add an entry to your routing table that will be permanent, run the route add command with the –p option. Omitting that, the entry will be lost at next reboot:
  route add 0.0.0.0 mask 0.0.0.0 172.16.250.5 –p
Here’s a simple way to see all open network connections, refreshing every second:
  netstat –ano 1
You can use the shutdown to shutdown or reboot a machine, including your own, in a simple scheduled task like this:
  shutdown –r –t 0 –m \\localhost

## Slide 42: Basic Wireless Router Configuration
3Com Router

## Slide 43: Network Cabling
Ethernet Cabling

## Slide 44: Wireshark
Network Analysis Tool